## Slide 1
PREDICTIVE MAINTENANCE — PIPELINE ARCHITECTURE
Dual-path tire failure prediction: ML anomaly detection + physics-based slow leak filtering
← INSERT ARCHITECTURE DIAGRAM: Redshift → Root ETL → [ML Path | Filter Path] → Alerts →
DATA SOURCE
Redshift Datashare (MMT telemetry)
Hourly SQL query via Lambda → S3
Fields: pressure, temperature,
vehicle_id, tire_id, timestamp
ROOT ETL
Glue Spark job (hourly, 30min offset)
Clean · convert units · weave tables
Output: S3 partitioned by date/hour
Feeds both ML and Filtering paths
ML PATH
Daily ML ETL → resample to 1-day
Engineer: delta_pressure, delta_temp
Normalize: z-score (Welford's → SSM)
SageMaker RCF → anomaly scores
FILTERING PATH
Nightly Step Function → Glue job
Quantile filter (10th pctl rolling)
Leak rate = ΔPSI / Δdays
Severity: H>3 · M>2 · L>1 PSI/day
ALERTS SYSTEM
Both paths → S3 upload triggers alerts-transformer Lambda → DynamoDB (PENDING) → SQS → processor (PROCESSED) → DLQ → cleaner (FAILED)
ML threshold: 99th percentile of batch scores, stored in SSM · Filtering: severity classification + time-to-80-PSI estimate
7-14 day advance warning · 4 features (pressure, temp, Δp, Δt) · Dual-path validation · 99th percentile threshold · 3 severity levels · DynamoDB alert lifecycle
© 2026, Amazon Web Services, Inc. or its affiliates. All rights reserved.