## Slide 1
PREDICTIVE MAINTENANCE DEEP DIVE
ML-based tire failure prediction with 7-14 day advance warning using dual-path validation
IoT Core Ingestion
MQTT protocol · Tire pressure · Tread depth · Temperature
Vehicle TCU → IoT Core → IoT Rules Engine → Kinesis Data Streams
Feature Engineering
Glue ETL · S3 Feature Store
Rolling averages · Rate of change · Seasonal adjustments · Fleet baselines
DUAL-PATH VALIDATION
ML Anomaly Detection
SageMaker Random Cut Forest
• Unsupervised anomaly scoring
• Multi-variate time series
• Anomaly score threshold: 3σ
• Trained on 12 months fleet data
Physics-Based Filters
Statistical validation layer
• Pressure decay rate > 0.5 psi/day
• Tread depth below 3/32"
• Temperature anomaly correlation
• Eliminates sensor noise / false pos
Validated Alert
Both paths must agree → high-confidence prediction
Real-time SageMaker endpoint + batch scoring pipeline via Step Functions
PREDICTION TIMELINE
Day 0
Normal operation All readings nominal
Day 7-10
Early anomaly detected ML score crosses threshold
Day 10-12
Physics filter confirms Pressure decay validated
Day 12-14
Alert triggered Service appointment scheduled
Day 14+
Without prediction: Roadside failure
OUTCOMES
7-14 day advance warning
before tire failure occurs
False positive reduction via dual-path
ML alone: ~15% FP → Dual-path: <3% FP
Automated service scheduling
Alert → EventBridge → Connect outreach
7-14 days
advance warning
<3% FP rate
dual-path validated
Real-time
inference endpoint
Fleet-wide
batch scoring
Step Functions
orchestration
~$114/mo
total platform cost
© 2026, Amazon Web Services, Inc. or its affiliates. All rights reserved.